## Slide 1: Status Report #21
2020. 04. 03 (Fri)
B4 FUJIWARA Tomomasa

## Slide 2: Timing resolution vs. QDC
Checked Timing resolution vs. MIP
How to decide MIP of each scintillator
Uneven for both side
Evaluate geometric average of both MPPC
⇒ define “MIP” of the detector
2

## Slide 3: Decide MIP for scintillator
First, evaluate MIP for each MPPC
→ fit w/ landau+exp
Make dist.
Fit w/ landau+exp
evaluate MPV of landau
MIP = MPV × sqrt(R1.MIP × R2.MIP)

## Slide 4: Timing resolution vs. MIP (1) -from cable length dep.-
σdetector vs. MIP of ToFR
Error: only statistic by fitting
Slightly improve with increasing MIP value

## Slide 5: Timing resolution vs. MIP (2) –thickness & width dep.-
5t × 11w & 5t × 22w & 5t × 44w mm2
Vb – Vop = 0.0, +3.0, +6.0 V

## Slide 6
Fit w/
Converge minus value... ??
(look unphysical...)

## Slide 7
display to separate for each conditions
Look like to follow different function
It might have to deal individually ?

## Slide 9: New MPPC board
Future plan of 藤原ToF
Consideration of readout method (series or parallel)
Series connection (直列)
equivalent of series connection of capacitor
→ small time constant c.f.)
Necessary for large bias supply.
Parallel connection (並列)
Small bias supply
Large time constant

## Slide 10: New MPPC board
Soldering MPPC, resister etc.
Thank you so much Toyama-san

## Slide 11: Performance check
4MPPCs on board
At Vb = 196.0 V (~ 48 V 相当?)
Power supply
for OP amp
Bias supply
for MPPCs
Shading light w/ black sheet
10.0 nsec
10.0 mV
PM amp

## Slide 12: To do next
New board
  Install testbench & data taking.
Analysis of cosmic-lay data
  Consideration for charge & size dependence
Write B4 thesis.

## Slide 13: Back up

## Slide 17
―
Landau.Const = 2000.
Landau.MPV = 200.
Landau.Sigma = 50.
Exp.Const = 5.
Exp.Slope = -0.005
―
Landau.Const = 2000.
Landau.MPV = 200.
Landau.Sigma = 10.
Exp.Const = 5.
Exp.Slope = -0.005
―
Landau.Const = 2000.
Landau.MPV = 200.
Landau.Sigma = 20.
Exp.Const = 5.
Exp.Slope = -0.005