## Slide 1: Status Report #31
2020. 06. 11 (Fri)
Tohoku Univ. M1
Tomomasa FUJIWARA
Detector: Cosmic-ray
Simulation: Gap & Length size

## Slide 2: Cosmic-ray measurement
Last NKS2 meeting: Started data taking w/ new setup 3-scintillators
Logic:
Too low count rate...
~ 2000 counts/day
(I want ~10000 events at least to analysis...)

## Slide 3: Cosmic-ray measurement
New setup for data taking
Logic:
Event rate: ~4200/day
現在測定中

## Slide 4: Cosmic-ray measurement
Problem of DAQ
KiNOKOでのデータ収集: ランが始まるとkdfファイルが作られる
⇒ rootファイルに変換して解析
数日前からconstruct時に一瞬エラーが表示されるようになった
(エラー文をスクリーンショットしたはずなのだが保存できていなかった)
が, データ取得自体はスタートができていた(ので致命的な問題ではないと考えていた)
あとで確認するとkdfファイルが生成されていなかった
kdfファイルがある/dataディレクトリにファイルが多すぎることが原因だったらしい...
これまでの kdf ファイルを別名のディレクトリに移動させ空のdataディレクトリを作ることで対処

## Slide 5: Simulation (HyperNKS)
Assumption
Timing resolusion:
BLT: σ=100 psec
ToF: σ=150 psec
⇒ 解析時にroot上で乱数を振り分解能分だけぼかす
ブランチでの値: mean, 仮定した分解能: σのGaus
Position & momentum resolusion: Nothing
Detector size:
BLT: 200x × 100y [mm2]
non-sensivtive region: 6x × 3y [mm2]
(参考: 上原さんのSNP, 学会発表スライド)
*) http://lambda.phys.tohoku.ac.jp/~db/mediawiki/images/5/59/JPS_2019_Autumn_Oral_KeitaUehara_20190916.pdf
*) http://lambda.phys.tohoku.ac.jp/~db/mediawiki/images/a/a3/SNPSchool_2019_Oral_KeitaUehara_20190907.pdf
ここまで前々回と同じ
Particle | Number | Kinematics |  | 
 |  | Type | Momentum [MeV/c] | Angular [deg]
K+ | 100,000 | Kmaid: | ~ 900 - 500 | 0-180
π+ |  | Uniform at Target | 420 – 980 Central: 700 Range: 40% | 0 – 10
p |  |  |  | 
μ+ |  |  |  | 
e+ |  |  |  | 
Particle | Number | Kinematics |  | 
 |  | Type | Momentum [MeV/c] | Angular [deg]
K+ | 100,000 |  | ~ 900 - 500 | 0-180
π+ |  | Uniform at Target | 420 – 980 Central: 700 Range: 40% | 0 – 10
p |  |  |  | 
μ+ |  |  |  | 
e+ |  |  |  | 

## Slide 6: Simulation (HyperNKS)
Check number of Kaon detected at VD[2]
(ToF counterのつもり)
z-position, gap-size, length of scintillator
z=1500, 1750, 2000, 2250, 2500 2750, 3000 [mm]
Gap: ±0.0 - ±60.0 [mm] ⇒ step by 10.0 mm
Length: 300 - 550 [mm] ⇒ step by 50 mm
Make mass square 1d histogram.
Number of K+/Total K+ at target
Total: 7(z)×7(gap)×6(length) = 294 point

## Slide 7: Simulation (HyperNKS)
Check number of Kaon detected at VD[2]
(ToF counterのつもり)
z-position, gap-size, length of scintillator
z=1500, 1750, 2000, 2250, 2500 2750, 3000 [mm]
Gap: ±0.0 - ±60.0 [mm] ⇒ step by 10.0 mm
Length: 300 - 550 [mm] ⇒ step by 50 mm
Make mass square 1d histogram.
Check ratio: Number of K+/Total K+ at target
Total: 7(z)×7(gap)×6(length) = 294 point
Virtual detector
ToF wall
Total width: 2400 mm (assuming 20w mm × 120 )
ToF wall

## Slide 8: Simulation (HyperNKS)

## Slide 9: Simulation (HyperNKS)
1650 mm from yoke

## Slide 10: Simulation (HyperNKS)
Less than 1% ...
2150 mm from yoke

## Slide 11: Simulation (HyperNKS)
Check additional cut condition at VD[1]: CDC-size ⇒ 1600w × 630h [mm2] Ref: M. Kaneta et al., NIM A 886 (2018) 88-103
VD1

## Slide 12: Simulation (HyperNKS)
Result
⇒ the same value at all 294 points

## Slide 13
x-y plot at Virtual detector[2] (ToF) w/ BLT size (w/o ToF and CDC size)

## Slide 14
x-y plot at Virtual detector[2] (ToF) w/ BLT+CDC size (w/o ToF size)
the same value

## Slide 15
x-y plot at Virtual detector[2] (ToF) w/ BLT+CDC size (w/o ToF size)
the same value
NKS2後段で検出できるK+の最大数
⇒ BLT のサイズが決めている
⇒ そこからToF がどれだけ損失なく検出できるか

## Slide 16: To do next
Detector development
Data taking ⇒ まずは3月版基盤の性能確認 w/ MPPC×1
次に複数個読み出し
Simulation
Estimation e+/e- background from γ-ray
⇒ Check the dist. of e+/e- from near target at ToF position (backward NKS2)
⇒ Implementation material of target: liq.3,4He, window (Al or Be) (now: G4Garaxy)
Others

## Slide 22
2020. 06. 09 (Tue) 12:00
K+ × 1000000発飛ばしてたらなんかよくわからないエラーが出た。
一応ラン自体は終了した
rootファイルも生成されていてデータも入っているようだ